## Slide 1
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Brain-Inspired AI for Real-Time Heart Rhythm Monitoring
Accurate, Low-Power Arrhythmia Classification using Spiking Neural Networks (SNNs)
Author: Ketan Shinde | Domain: Neuromorphic AI & Healthcare Machine Learning
Notes: Good morning everyone. Today I am presenting our AI mini-project: a brain-inspired Spiking Neural Network designed for real-time heart rhythm monitoring. Instead of using heavy, power-hungry deep learning models, we use neuromorphic artificial intelligence that communicates through biological pulses to detect cardiac arrhythmias with over 97% accuracy while using very little computing power.

## Slide 2
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Problem Statement & Clinical Motivation
The Medical Need
• Heart diseases are the leading cause of mortality worldwide.
• Irregular heart rhythms (arrhythmias) can happen randomly and without warning.
• Patients need continuous 24/7 monitoring through small wearable patches.
• Catching dangerous heartbeats early prevents sudden cardiac arrest.
The Problem with Traditional AI
• Standard deep learning models (like CNNs or LSTMs) do massive continuous calculations.
• They consume heavy battery power, draining wearable monitors in just a few hours.
• Sending raw heart signals to the cloud introduces lag and risks patient privacy.
• We need an AI that can think locally on the wearable device in real time.
Notes: To introduce our motivation: heart disease is the number one cause of death globally. Dangerous heart conditions often strike suddenly, so patients need wearable heart monitors they can wear all day and night. However, standard AI models are too heavy for small battery devices—they drain batteries in hours and relying on cloud servers causes delays when a patient is in danger. Our goal was to create an intelligent model light enough to run right on the device.

## Slide 3
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Understanding Spiking Neural Networks (SNNs)
1. Brain-Inspired Pulses
• In our brains, neurons communicate using tiny electrical pulses called spikes.
• Instead of sending heavy decimal numbers, SNN neurons send simple on/off signals (0 or 1).
• Information is carried in the rhythm and timing of when these pulses fire.
2. The Leaky Bucket Analogy
• Think of each artificial neuron like a bucket with a small leak at the bottom.
• Incoming pulses add water into the bucket (Integrate).
• If nothing arrives, the level slowly drops over time (Leak).
• When the bucket fills to the top, it fires a pulse and resets to empty (Fire & Reset).
3. Why It Saves Power
• Neurons stay completely silent until an actual pulse arrives.
• No spikes = no activity = zero power consumed.
• Instead of complex multiplications, the network just does simple additions when a pulse hits.
• Ideal for smart, battery-powered medical wearables.
Notes: Here is the simple concept behind Spiking Neural Networks. In the human brain, neurons don't exchange large decimal numbers; they fire discrete electrical pulses. SNNs mimic this exact behavior. Each artificial neuron acts like a bucket with a tiny leak: it collects incoming signals, leaks if nothing arrives, and when it reaches a set threshold, it fires a pulse and resets to zero. Because neurons stay completely quiet when there is nothing to report, SNNs use almost zero power during quiet intervals.

## Slide 4
ARTIFICIAL INTELLIGENCE MINI-PROJECT
The Dataset: MIT-BIH Arrhythmia Benchmark
Benchmark: MIT-BIH Arrhythmia Database (PhysioNet)
Standard clinical benchmark with over 100,000 real patient heartbeats mapped to the 4 official AAMI medical categories:
Normal (N)
90,113 beats (89.5%)
Healthy sinus rhythm and typical heart patterns.
Supraventricular (S)
2,781 beats (2.8%)
Abnormal beats starting early in the upper heart chambers (atria).
Ventricular (V)
7,008 beats (7.0%)
Dangerous irregular contractions in the lower chambers (PVCs). Critical!
Fusion (F)
802 beats (0.8%)
A rare, complex blend of normal and ventricular heartbeats.
Notes: We tested our model on the MIT-BIH Arrhythmia Database, which is the international benchmark for heart classification. It contains over 100,000 beats divided into 4 official categories: Normal beats, Supraventricular beats from the upper chambers, Ventricular beats from the lower chambers which can be fatal, and rare Fusion beats. As you can see, almost 90% of beats are normal, which makes finding the rare arrhythmias a true needle-in-a-haystack problem.

## Slide 5
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Data Pipeline: From Raw Heartbeat to Brain Spikes
1. Slicing the Heartbeat
• We locate each heartbeat by finding its main sharp spike (the R-peak).
• We crop a neat window of 128 points around it.
• This captures the complete heartbeat wave from start to finish.
• Ensures every beat fed into the AI has identical length.
2. Cleaning the Signal
• Real heart signals get noisy when patients breathe, walk, or move.
• We apply a robust scaling filter that smoothly cleans up baseline drift.
• Scales every heartbeat neatly into a uniform 0 to 1 range.
• Ensures signals look clean and consistent for the neural network.
3. Converting to Spikes
• How does an SNN read a heartbeat? Using 'Rate Coding' across 25 time steps.
• Think of it like Morse code:
• • Tall peaks (QRS wave) → rapid, dense bursts of spikes.
• • Flat baseline → silent, almost zero spikes.
• Translates the heart signal into a rhythmic language the AI understands.
Notes: Here is our data pipeline in three straightforward steps. First, we slice out each heartbeat by finding the sharp R-peak and taking 128 points around it. Second, because real-world signals have baseline wander from breathing and motion, we clean and normalize the signal between 0 and 1. Finally, we convert those values into spikes using rate coding over 25 timesteps: the tall peaks produce rapid bursts of spikes, while the flat resting baseline stays quiet. It is essentially translating heartbeats into Morse code.

## Slide 6
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Network Architecture: Simple & Ultra-Compact
Layer Structure: 128 → 32 → 32 → 4
• Input Layer (128 channels): One input for each point in the heartbeat window.
• Hidden Layer 1 (32 neurons): Detects basic wave shapes and early rhythm patterns.
• Hidden Layer 2 (32 neurons): Combines patterns to spot specific arrhythmia traits.
• Output Layer (4 neurons): One neuron for each category (Normal, Supraventricular, Ventricular, Fusion).
• Winner Takes All: Whichever output neuron fires the most spikes is our final prediction!
Why the Design is So Efficient
✔ Tiny Memory Footprint: Total network size is only 5,248 parameters (roughly 5.2 Kilobytes!).
✔ Runs on Simple Microchips: Can easily fit into tiny, ultra-cheap microcontrollers or wearable chips without external memory.
✔ No Heavy Math: Calculations use simple additions rather than thousands of floating-point multiplications.
✔ Fast Response: Analyzes each heartbeat in a fraction of a millisecond.
Notes: Our neural network layout is clean and minimal. It has 128 inputs, two hidden layers of 32 neurons each, and 4 output neurons. Whichever output neuron fires the most spikes represents the diagnosed class. The most impressive aspect is its size: the entire model has only 5,248 parameters—taking up barely 5 kilobytes. This means it can easily live on a tiny wearable chip without needing extra RAM or cloud processing.

## Slide 7
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Training the AI: Overcoming the Spike Problem
The Challenge: Spikes Don't Have Slopes
• Modern AI normally learns using calculus slopes (gradients).
• When an AI makes an error, it follows the slope backwards to tweak its weights.
• The Problem with Spikes: A spike is an instant jump from 0 to 1.
• Because it is an instant cliff, the slope is flat everywhere—which normally halts AI learning completely!
• For decades, this made training spiking networks with deep learning nearly impossible.
The Solution: Surrogate Gradients
✔ The Clever AI Trick: We separate forward prediction from backwards learning.
✔ When running forward: The neurons use real, discrete binary spikes.
✔ When learning backwards: The computer pretends the sharp cliff is a smooth, gentle hill.
✔ This allows standard optimizers (like Adam) to calculate corrections smoothly.
✔ Result: We get real biological spikes with the training power of modern deep learning!
Notes: Here is the core technical challenge we solved. Deep learning algorithms rely on calculus slopes to learn from their mistakes. However, a spike is an abrupt jump from 0 to 1 with no smooth slope, which used to prevent backpropagation in spiking networks. We used a technique called Surrogate Gradient Learning: during the forward pass, the model uses real discrete spikes. During backward training, it substitutes a smooth mathematical curve. This clever trick lets the AI learn effortlessly using modern backpropagation.

## Slide 8
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Teaching the Rhythm: Timing-Aware Learning
Why Standard Loss Fails
• Normal classification loss only checks: 'Did the model pick the right label at the end?'
• It completely ignores how quickly or steadily the pulses fired.
• Cardiac diagnosis needs timing awareness, not just a final vote.
Teaching Rhythm & Timing
• We used a timing-aware loss function (Van Rossum distance).
• The model converts spike pulses into smooth activity waves over time.
• It compares its predicted rhythm against the correct rhythm at every single time step.
• Penalizes both missing a beat and firing too late.
The Training Result
• Smooth and reliable learning across all 60 training epochs.
• Total error dropped smoothly by ~71% from start to finish.
• The network learned to fire quickly and decisively when an arrhythmia appears.
Notes: To teach the network, we needed an objective function that cares about timing. Standard loss functions only ask whether the final answer was right, ignoring whether it fired early or late. We used a rhythm-aware metric called Van Rossum distance. It compares the continuous timing pattern of the model's spikes against the true rhythm across all 25 timesteps. This taught the network to fire cleanly and immediately when an arrhythmia occurs.

## Slide 9
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Experimental Results: Multi-Seed Benchmark
Model Version | Overall Accuracy | Balanced Score (F1) | Normal Detection | Arrhythmia Precision
Published SparrowSNN Baseline | 93.26 ± 0.82% | 71.14 ± 1.90% | 93.4% | ~50% (High false alarms)
Our Optimized SNN AI Model 🚀 | 97.24 ± 0.19% | 83.85 ± 1.36% | 98.57% | ~75% (Accurate & reliable)
97.24% ± 0.19%
Overall Accuracy
+3.98% over standard baseline
83.85% ± 1.36%
Macro-F1 Score
+12.71% balanced improvement
± 0.19%
Super Low Variance
Consistently high across random seeds
5.2 KB
Total AI Size
Fits on any microcontroller
Notes: Here are the final benchmark results across three independent test runs. The published baseline achieved 93.26% accuracy. Our optimized SNN surpassed this significantly, reaching 97.24% overall accuracy and an 83.85% balanced F1 score. Even more importantly, our standard deviation was just 0.19%, proving that the AI is rock solid and completely reproducible.

## Slide 10
ARTIFICIAL INTELLIGENCE MINI-PROJECT
Clinical Impact: Slashing False Alarms
Test Confusion Matrix (Over 20,000 Beats)
Pred N Pred S Pred V Pred F True N: 17,805 79 118 21 True S: 165 363 28 0 True V: 49 4 1,339 10 True F: 24 0 14 122 Key Highlights: • Healthy Beat Accuracy: 98.79% (Rarely causes false alarms) • Dangerous PVC Detection: 95.51% (Catches life-threatening beats) • High Arrhythmia Precision: ~75% to 81% true alert rate
Why This Matters in Healthcare
• Cutting False Alarms by ~46%: Drops nuisance alarms on healthy beats by nearly half, directly solving 'alarm fatigue' for nurses and doctors.
• Clinical Trust: When this system sounds an alarm, doctors know there is a 75-80% probability it is genuine, compared to only ~50% in prior models.
• Critical Sensitivity: Catches premature ventricular contractions with over 95.5% reliability, preventing progression to fatal ventricular fibrillation.
• Edge-Ready: All of this happens instantly on the patient's device.
Notes: Looking at the test confusion matrix on over 20,000 unseen patient beats: Normal beat accuracy is nearly 99%. In healthcare AI, false alarms are a major problem—if a monitor beeps constantly, patients ignore it. Our model reduced false alarms by nearly 46% while catching over 95.5% of dangerous ventricular arrhythmias. This proves our neuromorphic SNN delivers clinical-grade accuracy with ultra-low power and a tiny 5.2 KB footprint. Thank you, and I am happy to answer any questions.